CisteraScreenCapture

Platform: Windows7+, C#4.5

CisteraScreenCapture starts automatically and runs in the background permanently.
It has a systray icon. It writes log.
It has GUI to edit settings which is accessible only with Administrator privileges. GUI allows editing:
- server default ip;
- port listening to server;
- service domain to resolve by mDNS (default: .local.);
- service type to resolve by mDNS (default: _cisterascreencapturecontroller._tcp);
- captured video source (display, rectangular within virtual space, certain window);
- stop/run;
- exit;
The process requires Administrator privileges to exit.

CisteraScreenCapture monitors user login event. When a user logged in, it uses mDNS discovery to try to resolve the service name.

Then CisteraScreenCapture sends HTTP GET request:
 <ip received by mDNS response, otherwise a default preset ip>/screenCapture/register?username=<user name of logged in user>&ipaddress=<ip of client>&port=<client's port which is listening to server>

Also CisteraScreenCapture starts accepting TCP connections from the server which are used to exchange with messages. So, the server anytime after can send to CisteraScreenCapture a command to launch/stop ffmpeg streaming.

When the user logged off (check with multiple users), accepting TCP messages and ffmpeg stream if any, are terminated.

CisteraScreenCapture opens connection to the server when a user logged and keeps it alive while some user is logged. This connection is used by both CisteraScreenCapture and the server to exchange with messages.
If the connection breaks, CisteraScreenCapture tries to reconnect. If reconnecting failed, CisteraScreenCapture terminates ffmpeg streaming if it runs at the moment.

General message format for communicating between client and server:
request/response:
[message name+body length (2 bytes)][message name (ASCII string terminated with '\0')][message body, which is interpreted respectively to the message name]

Every request must get a response before sending next request. Responses have the same format as requests.

Messages:
direction	description	name	request body	response body
CisteraScreenCapture -> server	sent when a user logged in	LoggedUserName	the name of currently logged in user (ASCII string terminated with '\0')	OK or error message (ASCII string terminated with '\0')
CisteraScreenCapture -> server	polling to keep connection alive	Poll	nothing (0 bytes)	nothing (0 bytes)
server -> CisteraScreenCapture	The server turns on SSL on this TCP channel after receiving a success response. / The client turns on SSL after sending a success response.	SslStart	nothing (0 bytes)	nothing (0 bytes)
server -> CisteraScreenCapture	Launch ffmpeg stream to the server. If such a stream is running already, it will be terminated and a new one launched.	FfmpegStart	ffmpeg parameters string excluding ffmpeg itself (ASCII string terminated with '\0') / Comment: / The source of captured video (usually name of display but not only) is configurable on the client and should not be sent by the server. As ffmpeg arguments should go in certain order so, the client will look for -framerate in the string sent by the server and insert display parameters just after it.	OK or error message (ASCII string terminated with '\0')
server -> CisteraScreenCapture	stop ffmpeg	FfmpegStop	nothing (0 bytes)	OK or error message (ASCII string terminated with '\0')